NAME :Y.Vishnu Vardhan Reddy
ABSTRACT
ROLL NO :19731A04I2
SECTION :Henry
DEPARTMENT :ECE
TOPIC :MEMS SENSOR
INTRODUCTION:
MEMS-(Micro-electro-mechanical-system):As the name infers, Micro-electro-mechanical-Systems(MEMS) is the innovationthat consolidates electrical and mechanical frameworks at a miniaturized scale.Basically, any gadget created utilizing photograph lithography-based procedures with micrometer (1μm=10−6m) scale highlights that use both electrical and mechanical capacities could be viewed as MEMS.
TYPES OF GYROSCOPIC SENSORS :
1.Vibrating Gyroscopes :
Based on 1.‘Coriolis effect (linear vibrating gyroscopes)’
   2.‘Gyroscopic Precission (torsional vibrating guroscopes)’
2.Optical Gyroscopes :
Based on ‘Sagnac Effect’
MEMS is generally Vibrating Gyroscope.
APPLICATIONS:
■ This is MEMS gyroscope used in iPhone 4.
■ Used in input devices , Gaming and virtual reality devices.
■ Motion control with MMI (man-machine interface).
■ GPS navigation systems.
■ Appliances and robotics.
WORKING OF (L3G4200D) MEMS GYROSCOPE (x, y, z axis):
1) It consists of ‘four proof mass’ in the shape of a trapezium which lie in XY- plane.
2) It consists of 3 pairs of sense-modes in order to measure angular velocity in three axis x, y and z.
3) It has a drive-mode that will vibrate the 4 proof masses in and out.
4) Measuring the X-axis rotation(PITCH).
5) Measuring the Y-axis rotation(ROLL).
6) Measuring the Z-axis rotation(YAW).
SPECIFICATIONS:
• L3G4200D has a full scale -- (+250/+500/+2000dps(degrees per second))
• I 2 C/SPI digital output interface
• Data output -- (16 bits)
• Temperature -- (8 bits)
• Two digital output lines -- (interrupt and data ready)
• Integrated low- and high-pass filters -- (user selectable bandwidth)
• Wide supply voltage -- (2.4 V to 3.6 V)
• Embedded power-down and sleep mode
• Embedded temperature sensor
• High shock survivability
• Extended operating temperature range -- (-40 °C to +85 °C)
• Low voltage compatible IOs -- 1.8 V
CONCLUSION:
MEMS Gyroscope works based on the physical phenomenon called “Coriolis effect”.It is effect caused by Coriolis force which is an inertial or fictitious force that acts on objects that are in motion within a frame of reference that rotates with respect to an inertial frame.
The basic components present in MEMS Gyroscopes are :
1.Proof mass (a freely movable mass)
2.Drivers (which vibrate the proof mass)- by electrostatic forces
3. Sense-mode (senses the Coriolis force as a change in capacitance.